| TECHNICAL SPECIFICATION |
| --- |
| CABLE TYPE | LOW LOSS 200 COAXIAL CABLE |
| STRUCTURE |
|  | Composition(No./㎜) | 1/1.12mm |
| Conductor | Material | Bare Copper Wire |
|  | Outside Diameter (㎜) | 1.12(0.03mm |
|  | Material | Gas Injected Foamed Polyethylene |
| Insulation | Thickness (㎜) | 0.84mm |
|  | Nom. Diameter(㎜) | 2.80 ( 0.1mm |
| Shield | Material | (1) Bonded Aluminum Foil | (2) Tinned Copper Wire |
|  | Construction | 0.025mm | 16x6/0.12mm |
|  | Coverage |  | 88% |
|  | Diameter(㎜) |  | 0.12(0.008mm |
|  | Material | PVC |
| Jacket | Diameter(㎜) | 4.95 ( 0.10m |
|  | Color | Black |
| Printing | LOW LOSS 200 50 OHM COAXIAL CABLE NFC/HYT 3D |
| ELECTRICAL CHARACTERISTIC |
| Impedance | ( | 50 ( 3 |
| Insulation Resistance | M( / km | 1000 ( |
| Capacitance | pF/M | 80.4 ( 3 |
| Attenuation | Frequency(MHz) | 30 | 150 | 450 | 900 | 1500 | 1800 | 2500 |
|  | dB/100M | 5.8 | 13.1 | 22.8 | 32.6 | 42.4 | 46.6 | 55.4 |
| d. |  |
|  | DRWN. | Vivien Cheng | DRWN. No.: |
|  | CHKD. | C.H. Liu | 4LMR20009601001M1 |
|  | APPD. | Vincent Shen | Date:NOV. 05, 2004 |

# Text boxes

Jacket

Conductor

Insulation

Shield