CFD 400

Physical Characteristics

Type Nr. Inner Conductor O.D. in (mm) Dielectric O.D. in (mm) Outer Conductor O.D. in (mm) Standard Jacket in (mm) Weight kg/m CFD400 1/4" RG8/U JIS 8D type .109 (2.77) Copper-clad aluminum 1.41/Mft 4.60/km .285 (7.24) closed-cell PE .320 (8.13) Sealed Al./ Mylar*/Al.+ Tinned copper braid, 85% 1.65/ Mft 5.41/km .405 (10.3) Black PVC 0.108

Electrical Characteristics

Nominal Impedance (ohms) Nom. Velocity of propagation Capacitance pF / ft (pF/m) Nominal Attenuation MHz dB/ dB/ 100ft 100m 50 85% 24.0 (78.4) 30 150 450 900 1500 2000 2500 5500 .67 1.5 2.7 3.9 5.1 6.0 6.8 10.2 2.2 5.0 8.8 12.7 18.6 19.6 22.2 30.5